## Slide 1: A Wireless Home Automation System
Team 5
Peter Li
Wenxuan Qiu
Jing Bo Yang

## Slide 2: Project Overview

## Slide 3: Project Objectives
Lists of user commands & modules
Mechanical door demo
Controller board change: DCT module -> Logarithm module
Hub board changes: Custom modules for servo and relay switch control
Foreign language command support
Commands | PMODs in use
Open / Close door | Servos
Light On/Off | Relay switch
Enter | Servos, relay switch, distance sensor

## Slide 4: Controller Board Block Diagram
Microphone
Digilent Audio IP
DMA0
(AXI Stream)
Xilinx FFT IP
Xilinx Logarithm IP
Interrupt Controller
DDR3
Microblaze
Buttons
AXI Lite GPIO
DMA1
(AXI Stream)
DMA2
(AXI Stream)
Speaker
AXI Interconnect
Bluetooth
Digilent BT IP

## Slide 5: Peter’s Role: Hardware Setup on Controller Board
Hardware change: DCT module -> Logarithm module
Challenges:
  Bluetooth connection issues -> turn on Bluetooth modules at the same time
  Inconsistent / imprecise results from Xilinx FFT IP -> use full precision setting
  Inconsistent / imprecise results from Xilinx Log LP -> use max performance settings
  Large amount of noise in audio recording -> set consistent sampling rates in codec
Digilent / Xilinx IPs with custom-coded APIs
Lessons learned to ensure success:
  Each hardware recompile takes 20+ min
  Constantly backing up functional versions
  Test each interface individually before system integration
  Finalize hardware early to give more time for Jing Bo’s software implementation

## Slide 6: Voice Recognition Algorithm

## Slide 7: Voice Recognition Algorithm
VAD, FFT, then MFCC computation with Dynamic Time Wrap comparison
Innovation: dynamic time wrap with length penalty
Problems
  Audio samples must be collected from the same source (ADC quality)
  Alignment of audio snippets
  Computation efficiency
Lessons learned:
  Python needs to be carefully written to enable simply transferring to C
  Evaluation of processor computation capability before selecting algorithm

## Slide 8: Hub Board Block Diagram

## Slide 9: Hub FPGA Related Challenges
Controlling PMODs
  Hardware IPs
    Custom: Servo Controller, Relay Switch
    Digilent: MAXSONAR (ultrasonic sensor)
  Software control
    Template from sample projects
    Write individual features into C functions
Wooden door construction
  Prototype and revise as issues arise and alternatives are found
  Select the right material, tools, adhesives, and fasteners

## Slide 10: Thank you! Q&A Time

## Slide 11: Design Methodology
Modular design
  Breakdown the system into components that can be designed individually
  Integrate subsystems early and communicate frequently between team members
Git-based version control
  Maintain latest versions of working code
  Update weekly team meeting agenda and status
Prototyping
  Build Python / Verilog application for quick prototyping of required functions
  Prototype mechanical parts and revise design
Testing
  Have test plans for individual subsystems
  Individual IP component test bench and testing tools

## Slide 12: Bluetooth PMOD Testing
Initial testing: 2 PMOD on one FPGA
Final testing: 1 PMOD on each FPGA

## Slide 13: Servo Controller PMOD Testing
Servo angle controlled by switches

## Slide 15: Data Flow for Voice Recognition

## Slide 16: Initial Door Design

## Slide 17: Xilinx FFT Module Configuration 1
  16 bits fixed-point output -> not precise enough for our application

## Slide 18: Xilinx FFT Module Configuration 2
  Floating point output -> noisy output and uncontrollable output scaling

## Slide 19: Xilinx FFT Module Configuration 3
  32 bits full precision output -> less than 1% error compared with MATLAB FFT

## Slide 20: Hardware-acceleration for MFCC
Hardware Configuration | Time for MFCC | Percentage of time
Entirely on software | 8 min. | --
FFT IP implemented | 2 min 34 sec. | 32.08%
FFT & Logarithm IP implemented | 2 min 10 sec. | 27.08%